| Satellite / sensor name | Spectral Channels | Spectral Resolution | Spatial Resolution (sub-satellite) | Temporal Resolution | Orbit type and altitude |
| --- | --- | --- | --- | --- | --- |
| Spot 5 | P: panchromatic | 0.48-0.71µm | 2.5 to 5 m | 26 days | Sun-Synchronous 832 km |
|  | B1: green | 0.50-0.59 µm | 10 m |  |  |
|  | B2: red | 0.61-0.68 µm | 10 m |  |  |
|  | B3: near infrared | 0.78-0.89 µm | 10 m |  |  |
|  | B4: short-wave infrared (SWIR) | 1.58-1.75 µm | 20 m |  |  |
| Spot 4 | M: monospectral | 0.61-0.68 µm | 10 m |  |  |
|  | B1: green | 0.50-0.59 µm | 20 m |  |  |
|  | B2: red | 0.61-0.68 µm | 20 m |  |  |
|  | B3: near infrared | 0.78-0.89 µm | 20 m |  |  |
|  | B4: short-wave infrared (SWIR) | 1.58-1.75 µm | 20 m |  |  |
| Spot 1 | P: panchromatic | 0.50-0.73 µm | 10 m |  |  |
| Spot 2 | B1: green | 0.50-0.59 µm | 20 m |  |  |
| Spot 3 | B2: red | 0.61-0.68 µm | 20 m |  |  |
|  | B3: near infrared | 0.78-0.89 µm | 20 m |  |  |
| LandSat7 ETM | Band 1 blue | 0.45-0.52 µm | 30 m | 16 day | Sun-Synchronous 705 km |
|  | Band 2 green | 0.52-0.60 µm |  |  |  |
|  | Band 3 red | 0.63-0.69 µm |  |  |  |
|  | Band 4 near infrared | 0.76-0.90 µm |  |  |  |
|  | Band 5 mid-infrared | 1.55-1.75 µm |  |  |  |
|  | Band 6 Thermal infrared | 10.4-12.5 µm | 60 m |  |  |
|  | Band 7 Mid-infrared | 2.08-2.35 µm | 30 m |  |  |
|  | PAN | 0.50-0.90 µm | 15 m |  |  |
| MODIS | Band 1 | 0.620-0.670 µm | 250 m | 12 hours (??) | Sun-synchronous 705 km |
|  | Band 2 | 0.841-0.876 µm |  |  |  |
|  | Band 3 | 0.456-0.479 µm | 500 m |  |  |
|  | Band 4 | 0.545-0.565 µm |  |  |  |
|  | Band 5 | 1.23-1.25 µm |  |  |  |
|  | Band 6 | 1.628-1.652 µm |  |  |  |
|  | Band 7 | 2.105-2.155 µm |  |  |  |
|  | Band 8 | 0.405-0.420 µm | 1000 m |  |  |
|  | Band 9 | 0.438-0.448 µm |  |  |  |
|  | Band 10 | 0.483-0.493 µm |  |  |  |
|  | Band 11 | 0.526-0.536 µm |  |  |  |
|  | Band 12 | 0.546-0.556 µm |  |  |  |
|  | Band 13 | 0.662-0.672 µm |  |  |  |
|  | Band 14 | 0.673-0.683 µm |  |  |  |
|  | Band 15 | 0.743-0.753 µm |  |  |  |
|  | Band 16 | 0.862-0.877 µm |  |  |  |
|  | Band 17 | 0.890-0.920 µm |  |  |  |
|  | Band 18 | 0.931-0.941 µm |  |  |  |
|  | Band 19 | 0.915-0.965 µm |  |  |  |
|  | Band 20 | 3.660-3.840 µm |  |  |  |
|  | Band 21 | 3.929-3.989 µm |  |  |  |
|  | Band 22 | 3.929-3.989 µm |  |  |  |
|  | Band 23 | 4.020-4.080 µm |  |  |  |
|  | Band 24 | 4.443-4.498 µm |  |  |  |
|  | Band 25 | 4.482-4.549 µm |  |  |  |
|  | Band 26 | 1.360-1.390 µm |  |  |  |
|  | Band 27 | 6.535-6.895 µm |  |  |  |
|  | Band 28 | 7.175-7.475 µm |  |  |  |
|  | Band 29 | 8.4-8.7 µm |  |  |  |
|  | Band 30 | 9.58-9.88 µm |  |  |  |
|  | Band 31 | 10.78-11.28 µm |  |  |  |
|  | Band 32 | 11.77-12.2 µm |  |  |  |
|  | Band 33 | 13.185-13.485 µm |  |  |  |
|  | Band 34 | 13.485-13.785 µm |  |  |  |
|  | Band 35 | 13.785-14.085 µm |  |  |  |
|  | Band 36 | 14.085-14.385 µm |  |  |  |
|  | Meteosat/ SEVIRI | VIS 0.6 µm | 3000 m | 15 min |  |
|  |  | VIS 0.8 µm |  |  |  |
|  |  | IR 1.6 µm |  |  |  |
|  |  | IR 3.9 µm |  |  |  |
|  |  | WV 6.2 µm |  |  |  |
|  |  | WV 7.3 µm |  |  |  |
|  |  | IR 8.7 µm |  |  |  |
|  |  | IR 9.7 µm |  |  |  |
|  |  | IR 10.8 µm |  |  |  |
|  |  | IR 12.0 µm |  |  |  |
|  |  | IR 13.4 µm |  |  |  |
|  |  | HRV Broad-band high resolution visible | 1000 m |  |  |
|  | AVHRR | Ch 1 0.58-0.68 |  |  | sun-synchronous polar orbit with a nominal flight height of 833 km |
|  |  | Ch 2 0.725-1.0 |  |  |  |
|  |  | Ch 3 3.55-3.93 |  |  |  |
|  |  | Ch 4 10.3-11.3 |  |  |  |
|  |  | Ch 5 11.5-12.5 |  |  |  |
|  | ATSR | Band 1 (MWIR) 3.7 | 1000 m |  |  |
|  |  | Band 2 (TIR) 10.8 |  |  |  |
|  |  | Band 3 (TIR) 12 |  |  |  |
|  |  | Band 4 (VIS) 0.555 |  |  |  |
|  |  | Band 5 (VIS) 0.659 |  |  |  |
|  |  | Band 6 (NIR) 0.865 |  |  |  |
|  |  | Band 7 (SWIR) 1.61 |  |  |  |